## Slide 1: ChemTab: Integrated Framework for joint Reduced Basis Learning & Regression Learning using Shallow Autoencoder and Deep Regressor Author(s) Amol Salunkhe, Dwyer Deighan, Paul Desjardin, Varun Chandola Email: aas22@buffalo.edu, dwyerdei@buffalo.edu, ped3@buffalo.edu, chandola@buffalo.edu
Introduction
Chemistry Tabulation/Reduced Basis Learning
The thermochemical manifold is parameterized :
  Conserved scalar (mixture fraction, Z)
  Reaction progress variables
The reaction progress variable “C” calculated
  Intrinsic low dimensional manifold
  Flame Generation Manifolds (FGM)
Guiding principles for “C”
  Resulting transport equation that can be conveniently solved
  Reactive scalars should evolve on comparable time scales
  Parameters should be independent of each other
  A bijective mapping between spaces
Results
All the ML Frameworks perform better than the current framework
Acknowledgements
Funded by the United States Department of Energy’s (DoE) National Nuclear Security Administration (NNSA) under the Predictive Science Academic Alliance Program III (PSAAP III) at the University at Buffalo, under contract number DE-NA0003961.
The Physics Constrained DNN II combines the two steps into a coupled neural network architecture
The first layer can be conceptualized as a Linear Shallow Autoencoder which does Reduced Basis Learning (learn linear embedding from input high-dimensional input vector )
The subsequent layers form a Deep Regressor that predicts the target state variables (source energy, temperature, etc.) from the linear embedding
Both networks are jointly trained
References
Formulation and assessment of flamelet generated manifolds for reacting interfaces
Regularization of reaction progress variable for application to flamelet based combustion models
Combustion modeling using principal component analysis
Physics-guided Neural Networks (PGNN): An Application in Lake Temperature Modeling
Combustion modeling using Principal Component Analysis: A posteriori validation on Sandia flames
Future Work
To incorporate the 1-D Flame Generation to the DNN as a part of the Physics Constraint
To Expand the DNN to give confidence intervals around the point estimates
To create a Gaussian Process based joint framework
Summary
The Physics Constrained Deep Neural Network II (PCDNN II) shows quantitatively accurate predictions for source energy terms and is comparable in performance to the PCA and GP Framework.
This is a significant first step in creation of a broader framework that helps jointly optimize reduced basis learning and reverse lookup learning
ML predictive model
Thermochemical state variables
Run-time
High dimensional input vector
Low-dimensional state
Pre-computation
Constrained PCA
Existing Framework
Reduced Basis Parameterization in 2 dimensions: Zmix, C
Tabulation using Conformal Mapping
Reverse Lookup using Lagrange Polynomial Interpolation
Method | Total Absolute Error | Mean Absolute Error
Non-ML Framework | 3.68E+13 | 2.24E+09
ML Framework I (GP) | 3.98E+12 | 4.84E+08
ML Framework I (DNN) | 3.36E+12 | 4.09E+08
Physics Constrained DNN Framework I | 6.94E+12 | 8.44E+08
Physics Constrained DNN Framework II | 3.94E+12 | 4.04E+08
Reduced Basis Learning
Reverse Lookup Learning
Reduced Basis Learning
Reverse Lookup Learning
Reduced Basis Learning
Reverse Lookup Learning
Combustion Modelling
Chemistry
Modelling
Flow
Modelling
Machine Learning Framework
(re) Solved Separately for Computational Efficiency
Physics Constrained DNN Framework II
Issues
In order to satisfy (bijective mapping), several flames in the original data are removed before building the look-up table
  Inaccurate estimation of the thermochemical space
This could be improved by including more progress variables
  Would make interpolation even more inefficient
  Polynomial growth of the look-up table
Machine Learning Framework I
Fixed Expressions
Data Driven Calculations
High dimensional input vector
Thermochemical state variables
PCA reduced representation
Neural network 2
Linear layer
Neural network 1
Physics Constrained DNN Framework I
High dimensional input vector
Thermochemical state variables
Neural network
AutoEncoder
Kernel Constraints
Activity Regularizer
Regressor
Prediction
Loss
Regularizer
Reduced Basis Learning
Reverse Lookup Learning
The linear embedding is trained with following constraints:
  Unit Norm
  Orthogonality of Basis Vectors (weights)
  Uncorrelated Features (covariance of outputs from the linear layer)
The constraints get added to the Prediction Cost Function and aid in Joint Optimization