## Slide 1: Turbulent Combustion Modeling
Numerical simulations of turbulent combustion problems is expensive
  Large number of molecular species present
  Large disparity between the scales for the flame (combustion) and the flow
A typical model reduction strategy is to project the high-dimensional thermochemical state-space on a low-dimensional manifold
  The state-space is precomputed and parameterized in terms of a reduced set of scalar variables (tabulation)
  The flow system is solved using the scalar variables (model reduction)
  The full state space (chemistry) is efficiently looked up during run-time
Advantage: decouple the turbulent flow field (exists at a coarser time/spatial scale) and the chemical reactions (exist at a much finer time/spatial scale)
Src: S. Bhalla et al., 2019, ECML-PKDD

## Slide 2: Tabulation Famework Properties
Accuracy
Memory Efficiency
Speed
Interpretability
Uncertainty Quantification

## Slide 3: Reducing Chemistry
The thermochemical manifold is parameterized using:
  Conserved scalar (mixture fraction, Z)
  Reaction progress variables (e.g., Cpv in Bojko and Desjardin, 2016)
The reaction progress variable, C, can be calculated in several ways
  Intrinsic low dimensional manifold (ILDM – Mass and Pope, 1992)
  Flame Generation Manifolds (FGM)
Guiding principles for C
  C1 - Result in transport equation that can be conveniently solved
  C2 - The reactive scalars should evolve on comparable time scales
  C3 - Parameters should be independent of each other
  C4 - A bijective mapping from manifold space to the thermo-chemical state space

## Slide 4: Example of existing approaches
  Fixed expressions
  Data-driven calculations
  The weights are estimated by optimizing over a cost-function that imposes the monotonicity requirement (for C4)

## Slide 5: Issues
The look-up could be computationally inefficient
In order to satisfy C4 (bijective mapping), several flames in the original data are removed before building the look-up table
  Inaccurate estimation of the thermochemical space
This could be improved by including more progress variables
  Would make interpolation even more inefficient
  Exponential growth of the look-up table

## Slide 6
FLAMELET GENERATION
MANIFOLD GENERATION
LIBRARY
CFD
Dimensionality Reduction
Tabulation
Chemistry
(Precomputed)
Flow
(Run-time lookup)
Lagrange Polynomial Interpolation
Cpv
Zmix
Zst
Yi
Souspeci
……
….

## Slide 7
Machine Learning Framework
Reduced Basis Learning
Reverse Lookup Learning
Combustion Modelling
Chemistry
Modelling
Flow
Modelling
(re) Solved Separately for Computational Efficiency

## Slide 8
ML predictive model
Thermochemical state variables
Reverse Lookup Learning
High dimensional input vector
Low-dimensional state
Reduced Basis Learning
Constrained PCA
Simple ML Framework
Reduced Basis Learning
Regression Function Learning

## Slide 9
True vs Residuals

## Slide 10
High dimensional input vector
Thermochemical state variables
PCA reduced representation
Neural network II
Linear layer
Neural network I
The second neural network is trained to recover the PCA based reduction of the high-dimensional input
Both networks are jointly trained
PCDNN v1

## Slide 11
True vs Residuals

## Slide 12
The linear embedding is trained with following constraints:
  Unit Norm
  Orthogonality of Basis Vectors (weights)
  Uncorrelated Features (covariance of outputs from the linear layer)
The constraints get added to the Prediction Cost Function and aid in Joint Optimization
High dimensional input vector
Thermochemical state variables
Kernel Constraints
Neural network
Linear layer (5)
Kernel Constraints + Activity Regularizer Loss + Prediction Loss
Activity Regularizer
Linear Layer O/P = (W (ip) + bias)
Zmix
Shallow Auto Encoder
PCDNN v2

## Slide 13: Linear Layer Embedding
Hypothesis
  The higher dimensional data is highly noisy
  Maximal Variance Capture based reduced basis learning passes on the noise
  Regression Functions may be overfitting as a result
  Regularization properties on the lower dimensional manifold will aid the regression (similar to Ihlme’s manifold regularization [slide #3])
Regularizers are used on the Embedding ( y = Wx + b )
  Kernel Regularizer— Reduces the weights W
  Unit Norm— The weights W should be between 0 - 1
  Activity Regularizer— Reduces the layer’s output y

## Slide 14
True vs Residuals

## Slide 15: Results
Method | MAE | TAE
Framework Absolute Min (using all data) | 2.23 E9 | 3.68 E13
Framework Actual | 5.20 E9 | 8.58 E13
PCA + GP | 4.48 E8 | 3.61 E12
PCA + DNN | 3.68 E8 | 3.03 E12
PCDNN v1 | 2.71 E9 | 3.48 E13
PCDNN v2 | 2.74 E8 | 2.255 E12