## Slide 1: ML Framework For Chemistry Tabulation & Lookup Author(s) Amol Salunkhe, Siddhant Aphale, Paul Desjardin, Varun Chandola Email: aas22@buffalo.edu, saphale@buffalo.edu, ped3@buffalo.edu, chandola@buffalo.edu
Introduction
Chemistry Tabulation/Reduced Basis Learning
The thermochemical manifold is parameterized :
  Conserved scalar (mixture fraction, Z)
  Reaction progress variables
The reaction progress variable “C” calculated
  Intrinsic low dimensional manifold
  Flame Generation Manifolds (FGM)
Guiding principles for “C”
  Resulting transport equation that can be conveniently solved
  Reactive scalars should evolve on comparable time scales
  Parameters should be independent of each other
  A bijective mapping between spaces
Results
All the ML Frameworks perform better than the current framework
Acknowledgements
Funded by the United States Department of Energy’s (DoE) National Nuclear Security Administration (NNSA) under the Predictive Science Academic Alliance Program III (PSAAP III) at the University at Buffalo, under contract number DE-NA0003961.
The Physics Constrained DNN combines the two steps into a coupled neural network architecture
The first neural network is trained to accurately predict the target state variables (source energy, temperature, etc.) from the input high-dimensional input vector
The first layer has a linear activation and a bottleneck – width of the layer corresponds to the dimensionality of the reduced space
The second neural network is trained to recover the PCA based reduction of the high-dimensional input
Both networks are jointly trained
References
Formulation and assessment of flamelet generated manifolds for reacting interfaces
Regularization of reaction progress variable for application to flamelet based combustion models
Combustion modeling using principal component analysis
Physics-guided Neural Networks (PGNN): An Application in Lake Temperature Modeling
Combustion modeling using Principal Component Analysis: A posteriori validation on Sandia flames
Future Work
To incorporate the 1-D Flame Generation to the DNN as a part of the Physics Constraint
To Include the Manifold Regularization in the DNN as a Physics Constraint
To create a Gaussian Process based joint framework
Summary
The Physics Constrained Deep Neural Network (PCDNN) shows quantitatively accurate predictions for source energy terms and is comparable in performance to the PCA and GP Framework.
This is a significant first step in creation of a broader framework that helps jointly optimize reduced basis learning and reverse lookup learning
High dimensional input vector
Thermochemical state variables
PCA reduced representation
Neural network 2
Linear layer
Neural network 1
ML predictive model
Thermochemical state variables
Run-time
High dimensional input vector
Low-dimensional state
Pre-computation
Constrained PCA
Existing Framework
Reduced Basis Parameterization in 2 dimensions: Zmix, C
Tabulation using Conformal Mapping
Reverse Lookup using Lagrange Polynomial Interpolation
Method | Total Absolute Error | Mean Absolute Error
Non-ML Framework | 3.68E+13 | 2.24E+09
ML Framework I (GP) | 3.98E+12 | 4.84E+08
ML Framework I (DNN) | 3.36E+12 | 4.09E+08
Physics Constrained DNN Framework | 6.94E+12 | 8.44E+08
Reduced Basis Learning
Reverse Lookup Learning
Reduced Basis Learning
Reverse Lookup Learning
Reduced Basis Learning
Reverse Lookup Learning
Combustion Modelling
Chemistry
Modelling
Flow
Modelling
Machine Learning Framework
(re) Solved Separately for Computational Efficiency
Physics Constrained DNN Framework
Issues
In order to satisfy (bijective mapping), several flames in the original data are removed before building the look-up table
  Inaccurate estimation of the thermochemical space
This could be improved by including more progress variables
  Would make interpolation even more inefficient
  Polynomial growth of the look-up table
ML Framework I
Step 1: Use principal component analysis (PCA) to learn the progress variables
  Orthogonal basis vectors (C3)
    A constrained PCA formulation used to include Zmix
Step 2: Replace Tabular Lookup using ML Model
  A Gaussian Process Regression model
    Also provides uncertainties with the predictions
    Computationally inefficient
  A neural network
    Could be computationally inefficient
The reduction and the ML model lookup steps are decoupled in the first framework
  PCA focuses on maximizing the variance of the high-dimensional data in the low-dimensional reduction (C1, C2, C3)
  Is not necessarily informed by the subsequent task of predicting the high-dimensional state (C4)
Machine Learning Framework I
Fixed Expressions
Data Driven Calculations