## Slide 1: Turbulent Combustion Modeling
Numerical simulations of turbulent combustion problems is expensive
  Large number of molecular species present
  Large disparity between the scales for the flame (combustion) and the flow
A typical model reduction strategy is to project the high-dimensional thermochemical state-space on a low-dimensional manifold
  The state-space is precomputed and parameterized in terms of a reduced set of scalar variables (tabulation)
  The flow system is solved using the scalar variables (model reduction)
  The full state space (chemistry) is efficiently looked up during run-time
Advantage: decouple the turbulent flow field (exists at a coarser time/spatial scale) and the chemical reactions (exist at a much finer time/spatial scale)
Src: S. Bhalla et al., 2019, ECML-PKDD

## Slide 2: Tabulation Famework Properties
Accuracy
Memory Efficiency
Speed
Interpretability
Uncertainty Quantification

## Slide 3: Reducing Chemistry
The thermochemical manifold is parameterized using:
  Conserved scalar (mixture fraction, Z)
  Reaction progress variables (e.g., Cpv in Bojko and Desjardin, 2016)
The reaction progress variable, C, can be calculated in several ways
  Intrinsic low dimensional manifold (ILDM – Mass and Pope, 1992)
  Flame Generation Manifolds (FGM)
Guiding principles for C
  C1 - Result in transport equation that can be conveniently solved
  C2 - The reactive scalars should evolve on comparable time scales
  C3 - Parameters should be independent of each other
  C4 - A bijective mapping from manifold space to the thermo-chemical state space

## Slide 4: Example of existing approaches
  Fixed expressions
  Data-driven calculations
  The weights are estimated by optimizing over a cost-function that imposes the monotonicity requirement (for C4)

## Slide 5: Issues
The look-up could be computationally inefficient
In order to satisfy C4 (bijective mapping), several flames in the original data are removed before building the look-up table
  Inaccurate estimation of the thermochemical space
This could be improved by including more progress variables
  Would make interpolation even more inefficient
  Exponential growth of the look-up table

## Slide 6: Proposed Machine Learning Based Framework 1
High dimensional input vector
Low-dimensional state
ML predictive model
Thermochemical state variables
Run-time
Pre-computation
Constrained PCA

## Slide 7: Proposed Machine Learning Based Framework 2
The second neural network is trained to recover the PCA based reduction of the high-dimensional input
Both networks are jointly trained
High dimensional input vector
Thermochemical state variables
PCA reduced representation
Neural network 1
Neural network 2
Linear layer

## Slide 8: Proposed Machine Learning Based Framework 2
The linear embedding is trained with following constraints:
  Unit Norm
  Orthogonality of Basis Vectors (weights)
  Uncorrelated Features (covariance of outputs from the linear layer)
The constraints get added to the Prediction Cost Function and aid in Joint Optimization
High dimensional input vector
Thermochemical state variables
Kernel Constraints
Neural network
Linear layer (5)
Kernel Constraints + Activity Regularizer Loss + Prediction Loss
Activity Regularizer
Linear Layer O/P = (W (ip) + bias)
Zmix

## Slide 9
Oxidizer
Fuel
Flame
x - Axial Coordinate
r - Radial Coordinate

## Slide 10
CHEMISTRY PDE DATA
MANIFOLD GENERATION
REVERSE LOOKUP
CFD
Dimensionality Reduction
Tabulation
Chemistry
(Precomputed)
Flow
(Run-time lookup)
Cpv
Zmix
Zst
Yi
Souspeci
……
….

## Slide 11
FLAMELET GENERATION
MANIFOLD GENERATION
LIBRARY
CFD
Dimensionality Reduction
Tabulation
Chemistry
(Precomputed)
Flow
(Run-time lookup)
Lagrange Polynomial Interpolation
Cpv
Zmix
Zst
Yi
Souspeci
……
….

## Slide 12
Machine Learning Framework
Reduced Basis Learning
Reverse Lookup Learning
Combustion Modelling
Chemistry
Modelling
Flow
Modelling
(re) Solved Separately for Computational Efficiency

## Slide 13
ML predictive model
Thermochemical state variables
Reverse Lookup Learning
High dimensional input vector
Low-dimensional state
Reduced Basis Learning
Constrained PCA

## Slide 14
High dimensional input vector
Thermochemical state variables
PCA reduced representation
Neural network II
Linear layer
Neural network I

## Slide 15
True vs Residuals

## Slide 16
True vs Residuals

## Slide 17
True vs Residuals

## Slide 18
True vs Residuals

## Slide 20
True vs Residuals